## Slide 1: Chapter 6: First-Hop Redundancy
CCNP SWITCH: Implementing Cisco IP Switched Networks
Notes: Cisco Networking Academy Program
CCNP ROUTE: Implementing IP Routing
Chapter 1: Routing Services

## Slide 2: Chapter 6 Objectives
Overview of FHRP and HSRP
Configure and verify VRRP
Configure and verify GLBP
Notes: Chapter 1 Objectives

## Slide 3: Overview of FHRP and HSRP

## Slide 4: Overview of FHRP and HSRP
The need for first-hop redundancy protocols
HSRP overview
HSRP state transitions
Aligning HSRP with STP topology
Configuring and tuning HSRP
Load sharing with HSRP
Options HSRP has for tracking
Configuring HSRP interface tracking
Configuring object tracking in combination with HSRP
Configuring HSRP authentication
Tuning HSRP timers
The differences between HSRP Versions 1 and 2

## Slide 5: The Need for First-Hop Redundancy
Network hosts are configured with a single default gateway IP address
If the router whose IP address serves as the default gateway to the network host fails, a network host will be unable to send packets to another subnet

## Slide 6: The Need for First-Hop Redundancy
With first-hop router redundancy, a set of routers or Layer 3 switches work together to present the illusion of a single virtual router to the hosts on the LAN.
By sharing an IP address and a MAC (Layer 2) address, two or more routers can act as a single “virtual” router

## Slide 7: HSRP Overview
When frames are to be sent from the workstation to the default gateway, the workstation uses ARP to resolve the MAC address that is associated with the IP address of the default gateway.
The ARP resolution will return the MAC address of the virtual router.
Frames that are sent to the MAC address of the virtual router can then be physically processed by an active router that is part of that virtual router group.
The physical router that forwards this traffic is transparent to the network hosts.
The redundancy protocol provides the mechanism for determining which router should take the active role in forwarding traffic and determining when that role must be taken over by a standby router.

## Slide 8: HSRP Overview
When the forwarding router or a link to it fails
The standby router stops seeing hello messages from the forwarding router.
The standby router assumes the role of the forwarding router.
As the new forwarding router assumes both the IP and MAC addresses of the virtual router, the end stations see no disruption in service.

## Slide 9: HSRP Overview
HSRP active and standby routers send hello messages to multicast address 224.0.0.2 (all routers) for Version 1, or 224.0.0.102 for Version 2, using User Datagram Protocol (UDP) port 1985.
Hello messages are used to communicate between routers in the HSRP group.
All the routers in the HSRP group need to be L2 adjacent so that hello packets can be exchanged.

## Slide 10: HSRP Router Roles
All the routers in an HSRP group have specific roles and interact in specific manners:
■ Virtual router
  An IP and MAC address pair that end devices have configured as their default gateway.
  The active router processes all packets and frames sent to the virtual router address.
  The virtual router processes no physical frames. There is one virtual router in an HSRP group.
■ Active router
  Within an HSRP group, one router is elected to be the active router.
  The active router physically forwards packets sent to the MAC address of the virtual router.
  There is one active router in an HSRP group.

## Slide 11: HSRP Router Roles
Standby router
  Listens for periodic hello messages. When the active router fails, the other HSRP routers stop seeing hello messages from the active router.
  The standby router then assumes the role of the active router. There is one standby router in an HSRP group.
Other routers
  There can be more than two routers in an HSRP group, but only one active and one standby router is possible.
  The other routers remain in the initial state, and if both the active and standby routers fail, all routers in the group contend for the active and standby router roles.

## Slide 12: HSRP Active Router Operation
Router A assumes the active role and forwards all frames addressed to the assigned HSRP MAC address of 0000.0c07.acxx, where xx is the HSRP group identifier.

## Slide 13: HSRP State Transition
Notes: A router in an HSRP group can be in one of these states: initial, listen, speak, standby, or active. When a router exists in one of these states, it performs the actions required for that state. Not all HSRP routers in the group will transition through all states. For example, if there are three routers in the HSRP group, the router that is not the standby or active router will remain in the listen state.
All routers begin in the initial state. This is the starting state, and it indicates that HSRP is not running. This state is entered via configuration change, such as when HSRP is disabled on an interface, or when an HSRP-enabled interface is first brought up (for instance, when the no shutdown command is issued).
The purpose of the listen state is to determine whether there are any active or standby routers already present in the group. In the speak state, the routers are actively participating in the election of the active router, standby router, or both.
Each router uses three timers for the HSRP hello messages. When a timer expires, the router transitions to a new HSRP state.
In the example shown in Figure 6-5 , router A starts. Because it is the first router in the subnet that is configured for standby group 1, it transits through the listen and speak states, and then becomes the active router. Router B starts after router A. While router B is in the listen state, router A is already assuming the standby and then the active role. Because there is an active router already present, router B assumes the standby role.

## Slide 14: HSRP State Transition
Notes: This state is entered via configuration change, such as when HSRP is disabled on an interface, or when an HSRP-enabled interface is first brought up (for instance, when the no shutdown command is issued).

## Slide 15: HSRP State Transition
When two routers participate in an election process, a priority can be configured to determine which router should become active.
Without specific priority configuration, each router has a default priority of 100, and the router with the highest IP address is elected as the active router.
Regardless of other router priorities or IP addresses, an active router will stay active by default.
A new election will occur only if the active router is removed.
When the standby router is removed, a new election is made to replace the standby router.
This behavior can change with the preempt option.

## Slide 16: Aligning HSRP with STP Topology
It is a good practice to configure the same Layer 3 switch to be both the spanning-tree root and the HSRP active router for a single VLAN.
This approach ensures that the Layer 2 forwarding path leads directly to the Layer 3 device that is the HSRP active gateway, thus achieving maximum efficiency.

## Slide 17: Configuring and Tuning HSRP

## Slide 18: Configuring and Tuning HSRP
Step 1. Configure R1’s Ethernet 0/1 (LAN-facing interface) with 192.168.1.3/24 IP address and HSRP standby IP of 192.168.1.1.
The IP of 192.168.1.1 is HSRP’s virtual IP address that is also configured as the default gateway IP address on PC 1 and PC 2:
R1(config)# interface ethernet 0/1
R1(config-if )# ip address 192.168.1.3 255.255.255.0
R1(config-if)# standby 1 ip 192.168.1.1
Step 2. Configure R2’s Ethernet 0/1 (LAN-facing interface) with 192.168.1.2/24 IP address and HSRP standby IP of 192.168.1.1.
Both R1 and R2 must have the same HSRP virtual IP address configured:
R2(config)# interface ethernet 0/1
R2(config-if)# ip address 192.168.1.2 255.255.255.0
R2(config-if)# standby 1 ip 192.168.1.1

## Slide 19: Verify the ARP table
Step 3. On R1, verify the ARP table:
R1# show ip arp

## Slide 20: Forwarding Through the Active Router

## Slide 21: Make R2 the Active Router
Configure R2’s HSRP group 1 with priority of 110:
R2(config)# interface ethernet 0/1
R2(config-if)# standby 1 priority 110
Configure R1’s and R2’s Ethernet 0/1 HSRP group 1 interfaces with preemption:
R1(config)# interface ethernet 0/1
R1(config-if)# standby 1 preempt
R2(config)# interface ethernet 0/1
R2(config-if)# standby 1 preempt

## Slide 22: Make R2 the Active Router
R2# show standby brief

## Slide 23: Router R2 Failure Scenario

## Slide 24: HSRP States After R2 Recover
Notes: With preemption disabled, which is the default behavior, R2 would not regain active status after coming back online.

## Slide 25: Load Sharing with HSRP

## Slide 26: Multigroup HSRP (MHSRP)

## Slide 27: Multigroup HSRP (MHSRP)

## Slide 28: The Need for Interface Tracking with HSRP
HSRP can track interfaces or objects and decrement priority if an interface or object fails.
Interface tracking enables the priority of a standby group router to be automatically adjusted, based on the availability of the router interfaces.
When a tracked interface becomes unavailable, the HSRP priority of the router is decreased.
When properly configured, the HSRP tracking feature ensures that a router with an unavailable key interface will relinquish the active router role.
When the conditions that are defined by the object are fulfilled, the router priority remains the same.
As soon as the verification that is defined by the object fails, the router priority is decremented.
The amount of decrease can be configured.
The default value is 10.

## Slide 29: HSRP Interface Tracking
HSRP has a built-in mechanism for detecting link failures and starting the HSRP reelection process.

## Slide 30: HSRP with Interface Tracking On

## Slide 31: HSRP Tracking Configuration
R2(config)# interface ethernet 0/1
R2(config-if)# ip address 192.168.10.2
R2(config-if)# standby 10 ip 192.168.10.1
R2(config-if)# standby 10 priority 110
R2(config-if)# standby 10 preempt
R2(config-if)# standby 10 track ethernet1/1 20

## Slide 32: HSRP Tracking Configuration Arguments

## Slide 33: HSRP and Object Tracking

## Slide 34: HSRP With Object Tracking

## Slide 35: HSRP and Object Tracking Configuration
First, define an IP SLA ICMP echo test:
R2(config)# ip sla 10
R2(config-ip-sla)# icmp-echo 192.168.3.2
R2(config-ip-sla-echo)# frequency 5
R2(config-ip-sla-echo)# ip sla schedule 10 life forever start-time now
Then create an object and track the IP SLA instance:
R2(config)# track 100 ip sla 10
Then configure HSRP to track an object and decrement priority if the test fails:
R2(config)# interface ethernet 0/1
R2(config-if)# standby 1 track 100 decrement 20

## Slide 36: Tracked objects
Tracked objects are defined in global configuration with the keyword track , followed by an object number.
Although IP SLA is just one of the options that can be tracked, as shown in the following syntax, you can track up to 500 objects:
Switch(congi)# track 1 ?
interface Select an interface to track
ip IP protocol
list Group objects in a list

## Slide 37: Tracked objects
Tracked objects offer a vast group of possibilities.
A few options that are commonly available include the following
An interface
  This performs a similar function like the HSRP interface tracking mechanism, but with advanced features. This tracking object can not only verify the interface status (line protocol) but also whether IP routing is enabled, whether an IP address is configured on the interface, and whether the interface state is up, before reporting to the tracking client that the interface is up.
IP route
  A tracked IP-route object is considered up and reachable when a routing table entry exists for the route and the route is accessible. To provide a common interface to tracking clients, route metric values are normalized to the range of 0 to 255, where 0 is connected and 255 is inaccessible. You can track route reachability, or even metric values, to determine best-path values to the target network.

## Slide 38: Tracked objects (continue)
IP SLA
  This special case allows you to track advanced parameters such as IP reachability, delay, or jitter.
A list of objects
  You can track several objects and interrelate their results to determine whether one or several of them should trigger the “success” or “fail” condition.

## Slide 39: Configuring HSRP Authentication
HSRP provides the following two types of authentication:
  Plain text
  Message digest 5 (MD5) algorithm
To configure plain-text authentication, use the following interface configuration command on HSRP peers:
Switch(config-if)# standby group authentication string
To configure MD5 authentication, use the following interface configuration command on HSRP peers:
Switch(config-if)# standby group authentication md5 key-string [ 0 | 7 ] string

## Slide 40: Configuring HSRP Authentication
To configure MD5 authentication using key chains, use the following command sequence:
Switch(config)# key chain chain-name
Switch(config-keychain)# key key-number
Switch(config-keychain-key)# key-string [ 0 | 7 ] string
Switch(config-keychain-key)# exit
Switch(config)# interface interface-slot/number
Switch(config-if)# standby group authentication md5 key-chain chain-name

## Slide 41: Tuning HSRP Timers
By default, the HSRP hello time is 3 seconds, and the hold time is 10 seconds, which means that the failover time could be as much as 10 seconds for clients to start communicating with the new default gateway.
In some cases, this interval may be excessive for application support.
The hello-time and the hold-time parameters are configurable.
To configure the time between the hello messages and the time before other group routers declare the active or standby router to be nonfunctioning, enter this command in the interface configuration mode:
Switch(config-if)# standby [ group-number ] timers [ msec ] hellotime [ msec ] holdtime
Notes: Note Decreasing the HSRP timers will enable you to detect a first-hop failure faster. However, shorter HSRP timers mean more HSRP hello packets, which in turn means more overhead traffic.
When configuring HSRP timers, make sure that they harmoniously match the othertimers that can influence which path is chosen to carry packets in your network.

## Slide 42: Preemption Delay
Preemption is an important feature of HSRP that allows the primary router to resume the active role when it comes back online after a failure or a maintenance event.
Preemption is a desired behavior as it forces a predictable routing path for the VLAN traffic during normal operations.
It also ensures that the Layer 3 forwarding path for a VLAN parallels the Layer 2 STP forwarding path whenever possible.
When a preempting device is rebooted, HSRP preemption communication should not begin until the distribution switch has established full connectivity to the rest of the network.
This situation allows the routing protocol convergence to occur more quickly, after the preferred router is in an active state.
To accomplish this, measure the system boot time and set the HSRP preemption delay to a value that is about 50 percent greater than device’s boot time

## Slide 43: Configuring HSRP Preemption Delay Timers
For example, if the boot time for the distribution device is 150 seconds, the preempt delay should be set to 225 seconds

## Slide 44: HSRP Versions
There are two HSRP versions available on most Cisco routers and Layer 3 switches:
  HSRPv1 and HSRPv2.
Version 1 is a default version on Cisco IOS devices.
HSRPv2 allows group numbers up to 4095, thus allowing you to use VLAN number as the group number.
HSRP Version 2 must be enabled on an interface before HSRP IPv6 can be configured.
HSRP Version 2 will not interoperate with HSRP Version 1.
All devices in an HSRP group must have the same version configured; otherwise, the hello messages are not understood.

## Slide 45: HSRP Versions
An interface cannot operate both Version 1 and Version 2 because they are mutually exclusive.
The MAC address of the virtual router and the multicast address for the hello messages are different with Version 2.
HSRPv2 uses the new IP multicast address 224.0.0.102 to send the hello packets instead of the multicast address of 224.0.0.2, which is used by Version 1.
To enable HSRP Version 2, enable the following configuration:
Switch(config-if) standby hsrp-number version 2

## Slide 46
Configuring Layer 3 Redundancy with VRRP

## Slide 47: Configuring Layer 3 Redundancy with VRRP
Upon completing this section, you will be able to do the following:
Describe the idea behind VRRP
Configure and verify VRRP
Describe the differences between HSRP and VRRP
Describe tracking options with VRRP
Configure VRRP interface object tracking

## Slide 48: About VRRP
VRRP is an open standard alternative to HSRP.
VRRP is similar to HSRP, both in operation and configuration.
The VRRP master is analogous to the HSRP active gateway, and the VRRP backup is analogous to the HSRP standby gateway.
A VRRP group has one master device and one or multiple backup devices.
A device with the highest priority is the elected master. Priority can be a number between 0 and 255.
  Priority value 0 has a special meaning; it indicates that the current master has stopped participating in VRRP.
  This setting is used to trigger backup devices to quickly transition to master without having to wait for the current master to time out.

## Slide 49: About VRRP
VRRP differs from HSRP in that it allows you to use an address of one of the physical VRRP group members as a virtual IP address.
  In this case, the device with the used physical address is a VRRP master whenever it is available.
The master is the only device that sends advertisements (analogous to HSRP hellos).
Advertisements are sent to the 224.0.0.18 multicast address, protocol number 112.
The default advertisement interval is 1 second. The default hold time is 3 seconds.
HSRP, in comparison, has the default hello timer set to 3 seconds and the hold timer to 10 seconds.
Like with HSRP, load sharing is also available with VRRP. Multiple virtual router groups can be configured
Contrary to HSRP, preemption is enabled by default with VRRP.
Notes: Although VRRP as per RFC 3768 does not support millisecond timers, Cisco devices allow you to configure millisecond timers.
You need to manually configure the millisecond timer values on both the master and the backup devices.
Use the millisecond timers only where absolutely necessary and with careful consideration and testing.
Millisecond values work only under favorable circumstances, and you must be aware that the use of the millisecond timer values restricts VRRP operation to Cisco devices only.

## Slide 50: About VRRP

## Slide 51: HSRP and VRRP Differences

## Slide 52: Configuring VRRP and Spotting the Differences from HSRP

## Slide 53: IP Addressing for the VRRP Configuration

## Slide 54: Configuring VRRP
Step 1. Configure R1’s Ethernet 0/1 with IP address 192.168.1.3 and VRRP virtual IP address 192.168.1.1:
R1(config)# interface ethernet 0/1
R1(config-if)# ip address 192.168.1.3 255.255.255.0
R1(config-if)# vrrp 1 ip 192.168.1.1
Configure R2’s Ethernet 0/1 with IP address of 192.168.1.2 and VRRP virtual IP address of 192.168.1.1:
R2(config)# interface ethernet 0/1
R2(config-if)# ip address 192.168.1.2 255.255.255.0
R2(config-if)# vrrp 1 ip 192.168.1.1
Step 2. Configure R2’s Ethernet 0/1 with VRRP priority of 110:
R2(config-if)# vrrp 1 priority 110

## Slide 55: Verify the VRRP Status

## Slide 56: VRRP and Authentication
Configure MD5 authentication for VRRP on R1’s Ethernet 0/1 interface:
R1(config)# interface ethernet 0/1
R1(config-if)# vrrp 1 authentication md5 key-string MyVRRP
%VRRP-4-BADAUTHTYPE: Bad authentication from 192.168.1.2, group 1, type 0, expected 254.
Configure MD5 authentication for VRRP on R2’s Ethernet 0/1 interface:
R2(config)# interface ethernet 0/1
R2(config-if)# vrrp 1 authentication md5 key-string MyVRRP
R1’s CLI:
%VRRP-6-STATECHANGE: Et0/1 Grp 1 state Master -> Backup
Notes: The VRRP standard that was defined in RFC 2338 used plain-text and MD5 authentication, which was later revoked in RFC 3768 and RFC 5798m. However, Cisco IOS devices still support authentication mechanisms. Cisco’s implementation follows RFC 2338 and provide the Cisco IOS commands to configure the VRRP authentication.

## Slide 57: Tracking and VRRP
VRRP does not have a native interface tracking mechanism but it does have the ability to track objects.

## Slide 58: Tracking and VRRP Configuration
Create a tracked object, where the status of the uplink interface is tracked:
R2(config)# track 1 interface ethernet 0/0 line-protocol
Configure VRRP to track previously created object and decrease VRRP priority by 20 should the uplink fail:
R2(config)# interface ethernet 0/1
R2(config-if)# vrrp 1 track 1 decrement 20

## Slide 59
Configuring Layer 3 Redundancy with GLBP

## Slide 60: Configuring Layer 3 Redundancy with GLBP
Upon completing this section, you will be able to do the following:
Describe the basic idea behind GLBP
Compare GLBP to HSRP
Describe the possible states of GLBP virtual gateway and virtual forwarder
Configure and verify GLBP
Understand GLBP operations
List and describe GLBP load-balancing options
Secure GLBP using authentication
Describe GLBP behavior in VLANs with running STP
Describe the system of weights and decrements in GLBP

## Slide 61: Introducing GLBP
GLBP shares some concepts with VRRP and HSRP, but the terminology differs, and its behavior is more dynamic and robust.
Although HSRP and VRRP provide gateway resiliency only the active router within the group forwards the traffic for the virtual MAC.
HSRP and VRRP can accomplish load sharing by manually specifying multiple groups and assigning multiple default gateways.
GLBP is a Cisco proprietary solution that allows for automatic selection and simultaneous use of multiple available gateways, in addition to automatic failover between those gateways.
Multiple routers share the load of packets that, from a client’s perspective, are sent to a single default gateway address.
There is also no need to configure a specific gateway address on an individual host. All hosts can use the same default gateway.
Notes: HSRP and VRRP can accomplish load sharing by manually specifying multiple groups and assigning multiple default gateways.
That, however, introduces overhead in the form of additional configuration as well as supporting services, such as Dynamic Host Configuration Protocol (DHCP). In addition, because of the manual assignment of the default gateway to the end hosts, load sharing is rarely equally balanced among all participating gateways.

## Slide 62: GLBP Roles
GLBP routers are divided into two roles: a gateway and a forwarder:
GLBP AVG (active virtual gateway)
  Members of a GLBP group elect one gateway to be the AVG for that group.
  Other group members provide a backup for the AVG when the AVG becomes unavailable; these will be in standby state.
  The AVG assigns a virtual MAC address to each member of the GLBP group.
  The AVG listens to the ARP requests for the default gateway IP and replies with a MAC address of one of the GLBP group members, thus load sharing traffic among all the group members.
GLBP AVF (active virtual forwarder)
  Each gateway assumes responsibility for forwarding packets that are sent to the virtual MAC address that is assigned to that gateway by the AVG.
  These gateways are known as AVFs. There can be up to four forwarders within a GLBP group.
  All other devices will be secondary forwarders, serving as backup if the current AVF fails.
  Forwarders that are forwarding traffic for a specific virtual MAC are in the active state and are called AVFs. Forwarders that are serving as backups are in the listen state.

## Slide 63: Comparing GLPB to HSRP

## Slide 64: GLBP States

## Slide 65: GLBP States (Gateway)
Following are the possible virtual gateway states:
Disabled: The virtual IP address has not been configured or learned, but there is some GLBP configuration.
Initial: The virtual IP address has been configured or learned, but configuration is not complete. The interface must be operational on Layer 3 and configured to route IP.
Listen: The virtual gateway is receiving hello packets. It is ready to change to speak state if the active or standby virtual gateway becomes unavailable.
Speak: The virtual gateway is trying to become the active or standby virtual gateway.
Standby: This gateway is next in line to be the active virtual gateway.
Active: This gateway is the AVG, and is responsible for responding to ARP requests for the virtual IP address.

## Slide 66: GLBP States (Forwarder)
The following are the possible virtual forwarder states:
Disabled: The virtual MAC address has not been assigned or learned. The disabled virtual forwarder will be deleted shortly. This state is transitory only.
Initial: The virtual MAC address is known but configuration of virtual forwarder is not complete. The interface must be operational on Layer 3 and configured to route IP.
Listen: This virtual forwarder is receiving hello packets and is ready to change to the active state if the active virtual forwarder becomes unavailable.
Active: This gateway is the AVF, and is responsible for forwarding packets sent to the virtual forwarder’s MAC address.

## Slide 67: Configuring and Verifying GLBP

## Slide 68: IP Addresses Used in GLBP Configuration

## Slide 69: GLBP Configuration
Configure R1’s Ethernet 0/1 with IP address of 192.168.1.3 and GLBP virtual IP address of 192.168.1.1:
R1(config)# interface ethernet 0/1
R1(config-if)# ip address 192.168.1.3 255.255.255.0
R1(config-if )# glbp 1 ip 192.168.1.1
Configure R2’s Ethernet 0/1 with IP address of 192.168.1.2 and GLBP virtual IP address of 192.168.1.1:
R2(config)# interface ethernet 0/1
R2(config-if)# ip address 192.168.1.2 255.255.255.0
R2(config-if)# glbp 1 ip 192.168.1.1

## Slide 70: GLBP Configuration
Configure R1’s Ethernet 0/1 with GLBP priority of 110 and enable preemption for both GLBP routers:
R1(config)# interface ethernet 0/1
R1(config-if)# glbp 1 priority 110
R1(config-if)# glbp 1 preempt
R2(config)# interface ethernet 0/1
R2(config-if)# glbp 1 preempt
Notes: Like with HSRP, but unlike with VRRP, GLBP has preemption disabled by default

## Slide 71: The virtual MAC addresses of GLBP
The virtual MAC addresses of GLBP are in the form of 0007.b4XX.XXYY.
XXXX is a 16-bit value that represents six 0 bits, followed by a 10-bit GLBP group number.
YY is an 8-bit value, and it represents the virtual forwarder number.
The AVG assigned forwarder 1 virtual MAC address of 0007. b400.0101 and forwarder 2 virtual MAC address of 0007.b400.0102

## Slide 72: GLBP Final Configuration

## Slide 73: GLBP Operation (ARP Request)

## Slide 74: GLBP Operation (ARP Reply)

## Slide 75: GLBP Operation (Traffic Flow)

## Slide 76: GLBP Operations: Failed R1 New Data Path
Notes: Although the virtual router at this moment has two different virtual MAC addresses to support function for two AVFs, it does not make sense to keep them both for a longer time period. AVG maintains two different timers for this purpose. The redirect timer is used to determine when the AVG will stop using the old virtual MAC address in ARP replies. The AVF that uses an old virtual MAC address continues to act as a gateway for any client that tries to use it. When the timeout timer expires, the old MAC address of the virtual router and the virtual forwarder are flushed from all GLBP peers. AVG assumes that old AVF will not return to service, so the resource (virtual MAC address) is reclaimed. Clients using an old MAC address must refresh the entry to obtain a new virtual MAC address. By default, the redirect timer is 10 minutes, and the timeout timer is 4 hours

## Slide 77: GLBP Load-Balancing Options
GLBP supports the following operational modes for load balancing traffic across multiple default routers that are servicing the same default gateway IP address:
Weighted load-balancing algorithm
  The amount of load that is directed to a router depends on the weighting value that is advertised by that router.
Host-dependent load-balancing algorithm
  A host is guaranteed the use of the same virtual MAC address as long as that virtual MAC address is participating in the GLBP group.
Round-robin load-balancing algorithm
  As clients send ARP requests to resolve the MAC address of the default gateway, the reply to each client contains the MAC address of the next possible router in a round-robin fashion. The MAC addresses of all routers take turns being included in address resolution replies for the default gateway IP address.
To configure the load-balancing option, use the following command:
  Switch(config-if)# glbp group load-balancing [ round-robin | weighted | host-dependent ]

## Slide 78: GLBP Authentication
The key for the MD5 hash can either be given directly in the configuration using a key string or supplied indirectly through a key chain.
The key string cannot exceed 100 characters in length.
The following example demonstrates the configuration for GLBP authentication:
Router(config)# interface Ethernet0/1
Router(config-if)# ip address 10.0.0.1 255.255.255.0
Router(config-if)# glbp 1 authentication md5 key-string d00b4r987654321a
Router(config-if)# glbp 1 ip 10.0.0.10

## Slide 79: GLBP and STP
With some switching topologies, the operation of STP results in inefficient traffic paths.
In such cases, implementation of HSRP might be preferred over GLBP because it is easier to understand, whereas GLBP provides no advantages.
Notes: Topologies with layer 2 loops (such as the one on Figure 6-32 , where distribution Layer 3 switches are interconnected) run STP, which blocks some of the access-distribution links. The end hosts now only have a direct connection with SW1.
In environments with STP and multiple VLANs, GLBP’s load sharing might not be of value, and the configuration of a multigroup HSRP aligned with STP topology may be preferred.

## Slide 80: Tracking and GLBP
Changing weight affects the AVF election and the load-balancing algorithm.
Both values can be manipulated with object tracking.

## Slide 81: GLBP Weight
GLBP uses a weighting scheme to determine the forwarding capacity of each router in the GLBP group.
The weighting that is assigned to a router in the GLBP group can be used to determine whether it will forward packets and, if so, the proportion of hosts in the LAN for which it will forward packets.
Thresholds can be set to disable forwarding when the weighting for a GLBP group falls below a certain value, and when it rises above another threshold, forwarding is automatically reenabled.
By default, the GLBP virtual forwarder preemptive scheme is enabled with a delay of 30 seconds.
A backup virtual forwarder can become the AVF if the current AVF weighting falls below the low weighting threshold for 30 seconds.
To disable the GLBP forwarder preemptive scheme, use the no glbp forwarder preempt command or change the delay by using the glbp forwarder preempt delay minimum command.

## Slide 82: GLBP Tracking Detects Interface Failure

## Slide 83: GLBP Weighing Option Under Failures
Notes: If load balancing is configured as round-robin, then, as long as both S1 and S2 are eligible to forward, traffic will be about 50:50 between both first hops.

## Slide 84: GLBP Object Tracking Sample Configuration

## Slide 85: Chapter 6 Summary
The redundancy protocol provides the mechanism for determining which router should take the active role in forwarding traffic and determining when that role must be taken over by a standby router .
HSRP is a Cisco proprietary protocol, whereas VRRP is an industry standard for virtual routing gateways.
HSRP Version 1 and Version 2 active and standby routers send hello messages to multicast address 224.0.0.2 for Version 1 and 224.0.0.102 for Version 2 on UDP port 1985.
It is important that the configured active router should be the same as the STP root bridge.
HSRP and VRRP use the VLAN load-balancing mechanism for load balancing.
With the new RFC, only the Cisco implementation of VRRP supports VRRP authentication.
GLBP, by default, provides the virtual gateway and load balancing via multiple virtual MAC addresses.
Review all the configuration examples and troubleshooting steps for better understanding and for exam preparation.

## Slide 86: Chapter 6 Labs
CCNPv7.1 SWITCH Lab6.1 FHRP HSRP VRRP
CCNPv7.1 SWITCH Lab6.2 HSRPv6
CCNPv7.1 SWITCH Lab6.3 GLBP

## Slide 88: Acknowledgment
Some of the images and texts are from Implementing Cisco IP Switched Networks (SWITCH) Foundation Learning Guide: (CCNP SWITCH 300-115) by Richard Froom and Erum Frahim (1587206641)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva