## Slide 1: Chapter 7: Network Management
CCNP SWITCH: Implementing Cisco IP Switched Networks
Notes: Cisco Networking Academy Program
CCNP ROUTE: Implementing IP Routing
Chapter 1: Routing Services

## Slide 2: Chapter 7 Objectives
This chapter covers the following topics related to network management and mobility:
AAA
Identity-based networking 802.1X
NTP
SNMP
Notes: Chapter 1 Objectives

## Slide 3: AAA

## Slide 4: AAA
■ Authentication
  Authentication is the process of identifying a user before that user is allowed access to a protected resource.
■ Authorization
  After the user gains access to the network, authorization is performed.
  Authorization allows you to control the level of access users have.
■ Accounting
  Accounting is performed after authentication. Accounting enables you to collect information about the user activity and resource consumption.

## Slide 5: AAA Benefits
Increased flexibility and control of access configuration
  AAA offers additional authorization flexibility on a per-command or per-interface level, which is unavailable with local credentials.
Scalability
  As the network grows, managing a large number of users on multiple devices becomes highly impractical and error-prone, with a lot of administrative burden.
Standardized authentication methods
  AAA supports the RADIUS protocol, which is an industry open standard. This ensures interoperability and allows flexibility because you can mix and match different vendors.
Multiple backup systems
  You may specify multiple servers when configuring authentication options on the method list, combining them in a server group.

## Slide 6: RADIUS and TACACS+ Overview
RADIUS and TACACS+ are AAA protocols.
Both use the client/server model.
As shown in Step 1, a user or machine sends a request to a networking device such as a router that acts as a network access server when running AAA.
The network access server then communicates (2, 3) with the server exchanging RADIUS or TACACS+ messages.
If authentication is successful, the user is granted (4) an access to a protected resource (5), such as a device CLI, network, and so on.
Notes: Cisco implements the AAA server functionality in the Cisco Secure Access Control Server (ACS) and Identity Services Engine (ISE), for example.

## Slide 7: TACACS+ Versus RADIUS

## Slide 8: RADIUS Authentication Process
Notes: 1 - RADIUS authentication process between the NAS and RADIUS server starts when a client sends a login request in the form of an Access- Request packet. This packet contains a username, encrypted password, the NAS IP address, and the NAS port number.
2 - When the RADIUS server receives the query, it first compares the shared secret key sent in the request packet with the value configured on the server. When shared secrets are not identical, the server silently drops the packet. This ensures that only authorized clients can communicate with the server. If shared secrets are identical, the packet is further processed, comparing the username and password inside the packet with those found in the database.
If a match is found, the server returns an Access-Accept packet with a list of attributes to be used with this session in the form of AV pairs (IP address, access control list [ACL] for NAS). If a match is not found, however, the RADIUS server returns an Access-Reject packet. It is important to notice that authentication and authorization phases are combined in a single Access-Request packet, unlike TACACS+.
During the authentication and authorization phase, an optional Access-Challenge message may be requested by the RADIUS server with the purpose of collecting additional data (PIN, token card, and so on), further verifying the client’s identity.
Moreover, the accounting phase is realized separately after the authentication and authorization phases, using Accounting-Request and Accounting-Response messages.

## Slide 9: TACACS+ Authentication Process
Notes: TACACS+ communication between the NAS and the TACACS+ server starts with a TCP communication, unlike RADIUS (which uses UDP).
Next, the NAS contacts the TACACS+ server to obtain a username prompt, which is then displayed to the user. The username entered by the user is forwarded to the server.
The server prompts the user again, this time for a password. The password is then sent to the server, where it is validated against the database (local or remote).
If a match is found, the TACACS+ server sends an ACCEPT message to the client, and the authorization phase may begin (if configured on the NAS). If a match is not found, however, the server responds with a REJECT message, and any further access is denied.

## Slide 10: Configuring AAA
To enable AAA, the first step is to configure the aaa new-model command in global configuration mode.
This step essentially enables AAA capability.
In addition, until this command is enabled, all other AAA commands are hidden.
The aaa new-model command immediately applies local authentication to all lines and interfaces (except console line con 0).
To avoid being locked out of the router, it is a best practice to define a local username and password before starting the AAA configuration.

## Slide 11: Configuring RADIUS Access
Switch(config)# radius server configuration-name
Switch(config-radius-server)# address ipv4 hostname [auth-port integer ] [ acct-port integer]
Switch(config-radius-server)# key string
Switch(config)# aaa group server radius group-name
Switch(config-sg-radius)# server name configuration-name
Notes: Configuration-name is just a text identifier for the server in question. In the subconfiguration, the DNS hostname or the IP address is specified.
Specification of a custom port number for the UDP communication is optional and rarely used for the case of leveraging nondefault ports.
The key string specifies the authentication and encryption key used between the access device and RADIUS server.
The next step is to add the RADIUS server to a server group. You can add multiple RADIUS servers to a group, as long as they were previously defined using the radius server command

## Slide 12: Apply RADIUS Method List to vty
Switch(config)# aaa authentication login radius_list group Mygroup2 local
Switch(config)# line vty 0
Switch(config-line)# login authentication radius_list

## Slide 13: Configuring TACACS+ for Console and vty Access
Switch(config)# tacacs server configuration-name
Switch(config-server-tacacs)# address ipv4 hostname
Switch(config-server-tacacs)# port integer
Switch(config-server-tacacs)# key string
Switch(config)# aaa group server tacacs+ group-name
Switch(config-sg-tacacs+)# server name configuration-name
Notes: The configuration-name is just a text identifier for the server in question. In the subconfiguration, the DNS hostname or the IP address of the server is specified.
Specification of a custom port number for the TCP communication is optional and used in the case of leveraging nondefault ports.
The key string specifies the authentication and encryption key used between the access device and TACACS+ server.

## Slide 14: AAA Authorization
To configure authorization, complete the following steps:
Step 1. Define a named list of authorization methods.
Step 2. Apply that list to one or more interfaces (except for the default method list).
Step 3. The first listed method is used. If it fails to respond, the second one is used, and so on until all listed methods are exhausted. Once the method list is exhausted, a failure message is logged.
Switch(config)# aaa authorization authorization-type list-name method-list
Switch(config)# line line-type line-number
Switch(config)# authorization { arap | commands level | exec | reverse-access } list-name
Notes: arap For Appletalk Remote Access Protocol
commands For exec (shell) commands
exec For starting an exec (shell)
reverse-access For reverse telnet connections

## Slide 15: AAA Accounting
AAA accounting has the same rules and configuration steps as authentication and authorization:
Step 1. You must first define a named list of accounting methods.
Step 2. Apply that list to one or more interfaces (except for the default method list).
Step 3. The first listed method is used; if it fails to respond, the second one is used, and so on.
Switch(config)# aaa accounting accounting-type list-name { start-stop | stop-only | none } method-list
Switch(config)# interface interface-type interface-number
Switch(config-if)# ppp accounting list-name

## Slide 16: Limitations of TACACS+ and RADIUS
RADIUS may not be the optimal choice in the following situations:
Device-to-device situations
  RADIUS does not offer two-way authentication.
Networks using multiple service
  RADIUS generally binds a user to a single service model.
TACACS+ may not be the optimal choice in the following situations:
Multivendor environment
  TACACS+ is a Cisco proprietary protocol
When speed of response from the AAA services is of concern
  TACACS+ uses TCP as a transport protocol mechanism.
Notes: Device-to-device situations
  RADIUS does not offer two-way authentication. It works strictly in a client/server mode, where authentication may be started only from the client side and where the server always authenticates the client. If you have two devices that need to mutually authenticate each other, RADIUS is not an appropriate solution.
Networks using multiple service
  RADIUS generally binds a user to a single service model. An Access-Request RADIUS packet contains information about a type of session you want to use. Two session types may be initiated: character mode (used for the Telnet service) and PPP mode (used for PPP). In character mode, your session will typically terminate on a device for the administrative purposes (for example, to access the CLI). In PPP mode, your session will terminate on a NAS, but your goal is to access network resources behind the NAS. A single RADIUS server cannot bind a user simultaneously to character and PPP mode.
Multivendor environment
  TACACS+ is a Cisco proprietary protocol developed as a completely new version of the older TACACS protocol. Some vendors may not support it even though Cisco has published TACACS+ specification in a form of a draft RFC.
When speed of response from the AAA services is of concern
  TACACS+ uses TCP as a transport protocol mechanism. TCP is a connection-oriented protocol, which means that a connection between two endpoints has to be established before the data can start to flow. On legacy devices, this mechanism may have higher latency, and TACACS+ might not be the best option if you need fast response from the AAA services. When using current-generation network devices and AAA servers, this is not an issue.

## Slide 17
Identity-Based Networking

## Slide 18: Identity-Based Networking
Identity-based networking is a concept that unites several features to include authentication, access control, mobility, and user policy components with the aim to provide and restrict users with the network services that they are entitled to.
From a switch perspective, identity-based networking allows you to verify users once they connect to a switch port..
Notes: From a switch perspective, identity-based networking allows you to verify users once they connect to a switch port. Identity-based networking authenticates users and places them in a specific VLAN based on their identity. Should any users fail to pass the authentication process, that user’s access can be rejected, or he might simply be put in a guest VLAN.

## Slide 19: IEEE 802.1X Port-Based Authentication Overview
Until the client is authenticated, 802.1X access control allows only EAPOL, Cisco Discovery Protocol (CDP), and Spanning Tree Protocol (STP) traffic to pass through the port to which the client is connected. After authentication is successful, normal traffic can pass through the respective port.

## Slide 20: 802.1X Client/Server Model
Client
  Usually a workstation or laptop with 802.1X-compliant client software.
  Most modern operating systems include native 802.1X support.
  The client is also referred to as a supplicant in 802.1X terminology.
Authenticator
  Usually an edge switch or wireless access point (AP), the authenticator controls the physical access to the network based on the authentication status of the client.
  Authenticator includes a RADIUS client, which is responsible for encapsulation and decapsulation of Extensible Authentication Protocol (EAP) frames and interaction with the authentication server.
Authentication server
  A server that performs the actual authentication of the client.
  Currently, a RADIUS server with EAP extensions is the only supported authentication server.

## Slide 21: 802.1X Port-Based Authentication Overview

## Slide 22: 802.1X Configuration Example
You will not be able to issue dot1x commands on the interface if it is not set to switchport mode access prior.
The default state of switch ports varies between switches, but it is not commonly set to the access mode.

## Slide 23
Network Time Protocols

## Slide 24: The Need for Accurate Time
The need for accurate time is increasing year by year.
Coordinating events, marking logs, and kicking-off scripts all run based on a system clock.
Therefore, in today’s network, coordination of system clocks and their accuracy is increasing in importance.
From a best practice perspective, it is recommended to set clocks on all network devices to UTC regardless of their location, and then configure the time zone to display the local time if desired. In this manner, global operations can fall back to UTC time for relative time.

## Slide 25: Configuring the System Clock Manually

## Slide 26: Setting Summer Time
clock summer-time zone recurring [ week day month hh:mm week day month hh:mm [offset]]
clock summer-time zone date date month year hh:mm date month year hh:mm [ offset ]
clock summer-time zone date month date year hh:mm month date year hh:mm [ offset ]

## Slide 27: Setting Summer Time

## Slide 28: Network Time Protocol Overview
Manually setting the clocks of any network device is neither accurate nor scalable.
The best practice is to use Network Time Protocol (NTP), Simple NTP (SNTP), or Precision Time Protocol (PTP)
NTP is designed to synchronize the time throughout an entire network infrastructure, including servers, switches, routers, host machines, wireless access points, uninterruptible power supply (UPS), and so on.
NTP leverages UDP port 123 for both the source and destination by default.
Notes: Sample NTP setup where the NTP is sourcing time from an atomic clock, Global Positioning System (GPS), or other accurate time source and sending NTP info out on the network to synchronize devices.

## Slide 29: Network Time Protocol Overview
An NTP network usually gets its reference time from an authoritative time source, such as a radio clock, GPS, or an atomic clock attached to an NTP time server somewhere in the network.
NTP then distributes this time across the network.
Accurate timekeeping is made possible by exchanging NTP messages between each pair of machines (server/client) with an association.
However, in a LAN environment, NTP can be configured to use IP broadcast messages instead.
To keep accuracy of time, NTP uses the concept of a stratum to describe how many NTP hops away a machine is from an authoritative time source.
A machine running NTP automatically chooses the machine with the lowest stratum number

## Slide 30: NTP: Stratum
NTP avoids in two ways synchronizing to a machine whose time may not be accurate.
  NTP never synchronizes to a machine that is not synchronized itself.
  NTP compares the time that is reported by several machines and will not synchronize to a machine whose time differs significantly from the others, even if its stratum is lower.

## Slide 31: NTP Modes
A device may take on more than one role at a time.
Server
  Provides accurate time information to clients on the network.
Client
  Synchronizes its time to an NTP server. This mode is most suited for file server and workstation clients that are not required to provide any form of time synchronization to other local clients. It can also provide accurate time to other devices.
Peers
  Peers only exchange time synchronization information.
Broadcast/multicast
  Special “push” mode of NTP server where the local LAN is flooded with updates; used only when time accuracy is not an issue.

## Slide 32: NTP Example

## Slide 33: Verify NTP

## Slide 34: Setting and Verifying the Clock Time Zone and Daylight Savings Time

## Slide 35: Downstream NTP Example

## Slide 36: NTP Design Principles
Notes: With a flat structure, all routers are configured to peer to each other as NTP peers. Each router will act both as a client and server with every other router. Two or three routers should be configured to synchronize their time with external time servers as a best practice to ensure redundancy to external time servers.
This model is very stable because each device synchronizes with every other device in the network. The disadvantages are difficulty of administration, slow convergence times, and poor scalability. If you add a device to the network, it can take you a good amount of time to identify all other devices and peer them with the new device. Because all devices in a peer-to-peer relationship have a say in selecting the best time, it can take some time for the routers to converge on an accurate time.
As a result, a flat NTP structure is not recommended for large networks. For large networks, it is a best practice to implement NTP in a hierarchical manner.
Internet service providers (ISPs) use this kind of hierarchical model to scale time synchronization.
Each ISP has multiple stratum 1 servers that synchronize to other ISP devices, and the ISP ultimately provides time synchronization services to customers’ devices on the edge of the network. The edge customer device then provides time synchronization to the rest of the internal customer network.
As a result, this tiered model consumes less administrative overhead and time convergence is minimized because every customer edge router is not associated with every other customer edge router. For large enterprise networks, it makes sense to implement a similar hierarchy of NTP synchronization.
A hybrid design of flat and hierarchical is referred to as a star structure, where all devices in a network have a relationship with a few time servers in the core. Figure 7-10 shows an example of a star design.

## Slide 37: Securing NTP
NTP authentication steps:
Step 1. Define NTP authentication key or keys with ntp authentication-key command. Every number specifies a unique NTP key.
Step 2. Enable NTP authentication using the ntp authenticate command.
Step 3. Tell the Cisco device which keys are valid for NTP authentication using the ntp trusted-key command. The only argument to this command is the key that you defined in the first step.
Step 4. Specify the NTP server that requires authentication by using the ntp server ip-address key key-number command. You can similarly authenticate NTP peers by using the ntp peer ip-address key key-number command.
Notes: Note that Cisco devices support only message digest 5 (MD5) algorithm authentication for NTP.

## Slide 38: NTP Authentication Example

## Slide 39: NTP ACL’s
For NTP, you can configure the following four restrictions through access lists:
Peer
  Time synchronization requests and control queries are allowed. The device is allowed to synchronize itself to remote systems that pass the access list.
Server:
  Time synchronization requests and control queries are allowed. The device is not allowed to synchronize itself to remote systems that pass the access list.
Server-only
  Only allows synchronization requests.
Query-only
  Only allows control queries.
Notes: As mentioned previously, once a Cisco router or switch has been synchronized to an NTP source, the Cisco router or switch will act as an NTP server to any device that requests NTP synchronization

## Slide 40: NTP Access List Example

## Slide 41: NTP Source Address
The source of the NTP packet will be the same as the interface the packet was sent out on.
When implementing authentication and access lists, it is good to have a specific interface set to act as the source interface for NTP.
It would be wise of you to choose a loopback interface to use as the NTP source.
This is because the loopback will never be down like physical interfaces.
If you configured loopback 0 to act as the NTP source for all communication and that interface has, for example, an IP address of 192.168.12.31, you can write up just one access list that will allow or deny based on one single IP address of 192.168.12.31.
Notes: SW-ACAD-ROOT(config)#ntp source interface-type interface-number

## Slide 42: NTP Versions
NTPv4 is an extension of NTP Version 3. NTPv4 supports both IPv4 and IPv6 and is backward compatible with NTPv3.
NTPv4 adds the following capabilities:
Support for IPv6
Better security
Leverages multicast over broadcast for push modes
Notes: Switch(config)# ntp server 2001:DB8:0:0:8:800:200C:417A version 4
NTPv4 provides the following capabilities:
NTPv4 supports IPv6, making NTP time synchronization possible over IPv6.
Security is improved over NTPv3. The NTPv4 protocol provides a whole security framework based on public key cryptography and standard X509 certificates.
Using specific multicast groups, NTPv4 can automatically calculate its timedistribution hierarchy through an entire network. NTPv4 automatically configures the hierarchy of the servers to achieve the best time accuracy for the lowest bandwidth cost. This feature leverages site-local IPv6 multicast addresses.

## Slide 43
SNMP

## Slide 44: SNMP
This subsection covers the following topics related to SNMP:
The role of SNMP
Different SNMP versions
Recommended practices for setting up SNMP
Configuration examples for SNMP Version 3
Verifying SNMP configurations

## Slide 45: SNMP Overview
SNMP systems consist of two components, as follows:
The SNMP manager that periodically polls the SNMP agents on managed devices by querying the device for data. Periodic polling has a disadvantage: A delay occurs between an actual event occurrence and the time the SNMP manager polls the data.
SNMP agents on managed devices collect device information and translate it into a compatible SNMP format according to the MIB. MIBs are collections of definitions of the managed objects. SNMP agents keep the database of values for definitions written in the MIB.
Notes: SNMP has become the standard for network management. SNMP is a simple, easy-toimplement protocol and is thus supported by nearly all vendors.
SNMP defines how management information is exchanged between SNMP managers and SNMP agents. SNMP uses the UDP transport mechanism to retrieve and send management information, such as Management Information Base (MIB) variables that contain information about the platform.

## Slide 46: SNMP Process
Notes: Therefore, SNMP polling is typically used to gather environment and performance data such as device CPU usage, memory usage, interface traffic, interface error rate, and so on. Free and enterprise-level NMS software bundles provide data collection, storage, manipulation, and presentation. An NMS offers a look into historical data, in addition to anticipated trends.
An NMS often supports a central view that provides an overview of the entire network to easily identify irregular events, such as increased traffic and devices unavailability due to DoS attacks.
These notifications are crucial to responding to attacks quickly.

## Slide 47: SNMP Versions
Version 1
  Introduced five message types
    Get Request,
    Get Next Request
    Set Request
    Get Response
    Trap.
  This version is rarely used nowadays.
Version 2
  Introduced two new message types
    Get Bulk Request to poll large amounts of data,
    Inform Request, a type of trap with expected acknowledgment on receipt.
  Version 2 added 64-bit counters to accommodate faster network interfaces.
  Added a complex security model, which was never widely accepted.
Version 2c
  Community-based SNMP Version 2, is wide accepted
  Community-based version of SNMP is very unsecure.
Version 3
  Methods to ensure the secure transmission of critical data between the manager and agent were added.

## Slide 48: SNMPv3 Security
SNMPv3 supports the following three levels of security:
noAuthNoPriv
  No authentication is required, and no privacy (encryption) is provided.
authNoPriv
  Authentication is based on Hashed Message Authentication Code (HMAC), MD5, or Secure Hash (SHA). No encryption is provided.
authPriv
  In addition to authentication, cipher block chaining - Data Encryption Standard (CBC-DES) encryption is used.

## Slide 49: SNMP Best Practices
Restrict access to read-only.
Use write access with separate credentials and careful consideration.
Set up SNMP views to restrict manager to only access needed sets of MIBs.
Configure ACLs to restrict SNMP access only by known managers.
Use SNMPv3 authentication, encryption, and integrity where possible, including upgrading devices to support SNMPv3 if necessary.

## Slide 50: SNMPv3 Configuration Steps
Step 1. Configure an access list to be used to restrict subnets for SNMP access.
Step 2. Configure the SNMPv3 views to limit access to specific MIBs.
Step 3. Configure the SNMPv3 security groups.
Step 4. Configure the SNMPv3 users.
Step 5. Configure the SNMPv3 trap receivers.
Step 6. Configure ifindex persistence to prevent ifindex changes.

## Slide 51: SNMPv3 Best Practice Configuration
Notes: The next step is to configure the restrictions to the MIBs. In Example 7-21 , a text label of OPS was configured for both the read and write view for the group groupZ. As in the example, only specific object identifiers (OIDs) are allowed in the view. For the example, the permitted OIDs system uptime, interface status, and descriptions were added.
The SNMPv3 group is configured with the authPriv security level ( snmp-server group groupZ v3 priv ), and the user for that group ( snmp-server userZ groupZ ) with passwords for both authentication ( auth sha itsasecret ) and encryption ( priv aes 256 anothersecret ).
The configuration example then enables SNMP traps with the snmp-server enable traps command. Traps are sent to an NMS or equivalent server; therefore, the receiving SNMP manager has to be configured. From the example, SNMPv3 traps will be sent to address 10.1.1.50 ( snmp-server host 10.1.1.50 traps ) using the user with the authPriv security level ( priv ). You can also limit events for which traps are sent. In the example, the traps are limited to CPU and port security-related events ( cpu port-security ).

## Slide 52: SNMP Command Reference

## Slide 53: Chapter 7 Summary
The AAA features include authentication, authorization, and accounting. The use of AAA is required in nearly all campus networks because it secures and provides administrative control and logging of user access to network devices and to the network itself.
Identity-based networking leverages protocols such as 802.1X to support mobility, security, authentication, and authorization of users to network resources.
Accurate time is essential for time logging services in campus networks, as are many security features like encryption.
All Cisco Catalyst switches support NTP for time synchronization.
NTP generally achieves millisecond accuracy in LAN networks.
SNMP is a lightweight protocol that not only monitors and controls devices but also supports alerting of events.
SNMPv3 is the best practice recommendation for SNMP; avoid using SNMPv2 (or v1) if it all possible (because of its lack of security features).
Security around SNMP must be considered as part of any implementation plan. At a minimum, use authentication and encryption along with restricted write access and IP ACLs to restrict network access.

## Slide 54: Chapter 7 Labs
CCNPv7.1 SWITCH Lab7.1 NTP
CCNPv7.1 SWITCH Lab7.2 SNMP

## Slide 56: Acknowledgment
Some of the images and texts are from Implementing Cisco IP Switched Networks (SWITCH) Foundation Learning Guide: (CCNP SWITCH 300-115) by Richard Froom and Erum Frahim (1587206641)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva